UNIVERSITY OF THE WEST INDIES

CAVE HILL CAMPUS

Department of Computer Science, Mathematics & Physics

# ELET3120 (EL31L) -  Communication Circuits

# Class Test 1						          Friday, February 15, 2013

- Give two reasons why audio is not transmitted at it’s original frequency.

- A 100W. carrier has 18W. of sideband power, what is the percentage of modulation ?

- What is the bandwidth of an AM signal when the highest modulating

frequency is 10kHz ?

- A 100V. p-p unmodulated carrier has a minimum amplitude of  20V. p-p when modulated , what is the maximum p-p voltage of the modulated waveform and what is the percentage of modulation ?

- What are the disadvantages of standard AM ?

- Give two uses of the Pi circuit.

- Give the characteristics of the Absorption Modulator and its typical usage.

- What is the purpose of a balanced modulator ?

- How much modulator power is required for 85% modulation of a 300kW amplifier ?

- Draw a labeled block diagram of a superheterodyne receiver ?

11.  What is the modulation index when a carrier is deviated 35kHz by a 7kHz signal ?

12.  If a receiver is tuned to a station at 980kHz and it’s IF is 455kHz what is the image

frequency and what is the local oscillator frequency ?

- With the aid of a diagram show how Frequency Modulation can be obtained from a

Phase Modulator.

14.  What factors must be considered when selecting an Intermediate Frequency  (IF) ?

15.  What is the purpose of a synchronous detector circuit  ?

16.  Define the terms sensitivity and selectivity as used in radio communications.

- When does maximum deviation occur in a phase modulated wave ?

- What is the purpose of an AGC circuit ?

- What is the Barkhausen Criterion ?

- What are three disadvantages of the tuned RF receiver ?